## Slide 1
Butterworth Low-Pass
Order 4 | Cutoff Frequency: 100 Hz
File 009 / 100 | Variant 9

## Slide 2
Filter Theory & Transfer Function
Transfer Function H(s) — Butterworth Order 4 |H(jω)|² = 1 / [1 + (ω/ωc)^8] ωc = 2π × 100 rad/s ≈ 628.3 rad/s 3 dB cutoff: 100 Hz Maximally flat passband (no ripple) Roll-off: 80 dB/decade beyond ωc

## Slide 3
Frequency Response — Bode Plot
Bode plot of Butterworth Low-Pass order 4 filter. Top panel: magnitude response in dB showing -3 dB cutoff at 100 Hz with a roll-off of approximately 80 dB/decade. Bottom panel: phase response in degrees.

## Slide 4
Circuit / Block Diagram
Sallen-Key topology for Butterworth Low-Pass order 4. The circuit uses two resistors R₁, R₂ and two capacitors C₁, C₂ around an op-amp in unity-gain configuration to realise a 2nd-order low-pass section with cutoff frequency 100 Hz.

## Slide 5
Design Parameters
Parameter | Value
Filter Family | Butterworth Low-Pass
Filter Type | Low-Pass
Filter Order (N) | 4
Cutoff Frequency (fc) | 100 Hz
Angular Cutoff (ωc) | 628.32 rad/s
Passband Gain (0 Hz) | 0 dB
-3 dB Frequency | 100 Hz
Roll-off Rate | 80 dB/decade

## Slide 6
Real-World Applications
• Anti-aliasing filter before ADC sampling in data acquisition systems • Audio signal smoothing in professional mixing consoles • DC power supply ripple rejection in instrumentation amplifiers • Vibration sensor conditioning in industrial IoT edge devices • Baseband filtering in software-defined radio (SDR) receivers
Filter: Butterworth Low-Pass | fc = 100 Hz | Order = 4