## Slide 1
Elliptic Low-Pass
Order 4 | Cutoff Frequency: 3,000 Hz | Passband Ripple: 0.5 dB
File 057 / 100 | Variant 7

## Slide 2
Filter Theory & Transfer Function
Transfer Function H(s) — Elliptic Order 4 |H(jω)|² = 1 / [1 + ε²·Rₙ²(ξ, ω/ωp)] ε² = 10^(Rp/10) - 1, Rp = 0.5 dB Rₙ = Chebyshev rational function ωp = 2π × 3,000 rad/s (passband edge) Equiripple in both passband and stopband Sharpest roll-off for given order and ripple

## Slide 3
Frequency Response — Bode Plot
Bode plot of Elliptic Low-Pass order 4 filter. Top panel: magnitude response in dB showing -3 dB cutoff at 3,000 Hz with a roll-off of approximately 80 dB/decade. Bottom panel: phase response in degrees.

## Slide 4
Circuit / Block Diagram
Cascade block diagram for Elliptic Low-Pass order 4. The design is decomposed into 2 second-order section(s), each realising a pair of complex conjugate poles near cutoff 3,000 Hz.

## Slide 5
Design Parameters
Parameter | Value
Filter Family | Elliptic Low-Pass
Filter Type | Low-Pass
Filter Order (N) | 4
Cutoff Frequency (fc) | 3,000 Hz
Angular Cutoff (ωc) | 18849.56 rad/s
Passband Gain (0 Hz) | 0 dB
-3 dB Frequency | 3,000 Hz
Roll-off Rate | 80 dB/decade
Passband Ripple | 0.5 dB

## Slide 6
Real-World Applications
• Narrowest transition band: satellite communication transponders • Multi-tone DTMF decoder front-end filtering • Anti-aliasing in high-speed ADCs where order must be minimised • Channel guard filtering in dense OFDM subcarrier spacing • Spectral containment in military frequency-hopping radios
Filter: Elliptic Low-Pass | fc = 3,000 Hz | Order = 4